# Plant Watering System Communication Specification
The plant watering system (PWS) exposes services that can be called remotely. The messages have a fixed length of 6 bytes and start and end with the ASCII characters STX and ETX. The remote system always initiates the communication and PWS replies with an ACK message informing the remote system whether the command was successfully carried out or not. If no ack is received within 2 seconds the remote system should re-send the message.
Message structure:

### Calculating the checksum
Modulo 256?
### ACK message
The message id for the ACK message is 0x00.
The parameters field contain an error code.

### Pump Control
The message id for turning pump on is 0x01.
The message id for turning pump off is 0x02.
Pump on timer is given in 0,1 seconds. The value 0x0021 means that the pump is on for 3,3 seconds. The value 0x0000 means that the pump is on until a stop command is received.

### Measure Moisture
The message for triggering a moisture measurement is 0x03.
The PWS first replies with an ACK and then measures the moisture.
After measuring the moisture the PWS sends the measurement data to the remote system with message id 0x04. The parameters field contain the measurement value.
No ack is sent by the remote system after receiving the measurement value. The remote system must send a new message with message id 0x03 if it failed to receive data.